# SECTION 01570 (01 57 00)

## TEMPORARY CONTROLS

GENERAL

SECTION INCLUDES

Erosion and Sediment Control.

Pest Control.

RELATED DOCUMENTS

Section 01110-Summary of Work:  Work sequence, Owner occupancy.

Section 01310-Project Management and Coordination:  Project coordination.

Section 01520-Construction Facilities:  Temporary buildings and other temporary facilities.

Section 01530-Temporary Construction:  Temporary construction.

Section 01560-Temporary Barriers and Enclosures.

Section 01740-Cleaning.

WATER CONTROL

Grade site to drain. Maintain excavations free of water.  Provide, operate, and maintain pumping equipment.

Protect site from puddling or running water.

Provide water barriers as required to protect site from soil erosion.

Dewatering Facilities and Drains:

For temporary drainage and dewatering facilities and operations not directly associated with construction activities included under individual specification sections, comply with dewatering requirements of applicable Division 2 Sections.

Where feasible, utilize the same facilities.

Maintain the site, excavations and construction free of water.

Comply with environmental limitations on dewatering as imposed by Broward County, the South Florida Water Management District, or other applicable jurisdictional authority.

EROSION AND SEDIMENT CONTROL

Plan and execute construction by methods to control surface drainage from cuts and fills, from borrow and waste disposal areas.  Prevent erosion and sedimentation.

Minimize amount of bare soil exposed at one time.

Provide temporary measures such as berms, dikes, and drains, to prevent water flow.

Construct fill and waste areas by selective placement to avoid erosive surface silts or clays.

Provide earthen embankments and similar barriers in and around excavations and subgrade construction sufficient to prevent flooding by runoff of storm water from heavy rains.

Periodically inspect earthwork to detect evidence of erosion and sedimentation; promptly apply corrective measures.

PEST CONTROL

Provide methods, means, and facilities to prevent pests, insects and rodents from infesting the area of the Work and adjacent premises.

Prior to construction of footings, foundations or slabs: Retain a local exterminator or pest control company to:

Recommend practices to minimize attraction and harboring of rodents, roaches and other pests.

Provide extermination and control procedures at regular intervals so the Project will be free of pests and their residues at Substantial Completion.

Ensure that pest, insect and rodent control operations are conducted in a lawful manner using environmentally safe materials.

Engage in exterminator to make final eradication of rodents, insects, and other pests as specified in Section 01570-Temporary Controls.

Repeat final treatments as necessary until Owner occupancy to ensure rodent, insect and pest free facilities.

Refer to Division 2 requirements for termiticide treatments and other pest control requirements.

REMOVAL OF UTILITIES, FACILITIES, AND CONTROLS

Remove temporary above grade or buried controls as warranted by the progress of the Work or prior to Substantial Completion.

Remove underground installations to a minimum depth of 2 feet.  Grade site as noted.

Clean and repair damage caused by installation or use of temporary work.

Restore existing facilities used during construction to original condition at start of work or as specified elsewhere in the Contract Documents.

Restore permanent facilities used during construction to specified condition.

PRODUCTS-Not Used

EXECUTION-Not Used

END OF SECTION