# SECTION 10675 (10 56 13)

## METAL STORAGE SHELVING AND CABINETS

GENERAL

SECTION INCLUDES

Metal storage shelving including storage cabinets, work benches, flammable liquid storage cabinets and necessary accessories indicated on the Drawings and specified in this Section.

RELATED SECTIONS

Section 01572-Construction Waste Management

Section 06100-Rough Carpentry.

Division 15 for venting for flammable liquid storage cabinets.

REFERENCES

International Organization for Standardization (ISO) 14021–1999; Environmental Labels and Declarations

(National Fire Protection Association) NFPA 30-Flammable and Combustible Liquids Code.

(Occupational Safety and Health Administration) OSHA 29

SUBMITTALS

Product Data:  Submit manufacturer’s catalog data and installation instructions for each type of item specified.

Recycled Content:

Indicate recycled content; indicate percentage of pre-consumer and post-consumer recycled content per unit of product.

Indicate relative dollar value of recycled content product to total dollar value of product included in project.

If recycled content product is part of an assembly, indicate the percentage of recycled content product in the assembly by weight.

If recycled content product is part of an assembly, indicate relative dollar value of recycled content product to total dollar value of assembly.

Shop Drawings:  Submit showing layout, details, dimensions and assembly and anchorage.  For flammable liquid storage cabinets, show ventilation connections.

QUALITY ASSURANCE

Provide certification that flammable liquid storage cabinets comply with OSHA 29 CFR 1910.106D and NFPA 30 requirements.

PRODUCTS

MANUFACTURERS

Subject to compliance with requirements, provide products of one of the following:

Equipto Steel Products.

Hallowell, division of List Industries.

Justrite, for flammable liquid storage.

Penco Products, Inc.

Tri-Boro Shelving.

MATERIALS

All metal storage and cabinet products are to contain recycled content.

Design and Construction:  18 gage clip-type adjustable shelving of modular unit construction of individual bolted frame assemblies, constructed in such a way that any section can be relocated and each shelf can be independently adjusted without the use of tools.

Shelving Unit Sizes:  Provide shelving in sizes as indicated on the Drawings.

Unit Sizes:

Type 1:  87 inches high x 12 inches deep, with top and six adjustable shelves, closed base fronts.

Type 2:  87 inches high x 18 inches deep, with top and six adjustable shelves, closed base fronts.

Type 3:  87 inches high x 24 inches deep, with top and six adjustable shelves, closed base fronts.

Above-noted Shelving:  Extend from wall to wall in rooms indicated on the Drawings to receive metal storage shelving.  Provide standard width units of 30 inches, 36 inches and 42 inches.

Provide metal shelving in Rooms as noted on the plans.

Wall Attachment Hardware:  Provide manufacturer’s recommended brackets and mounting screws for wall attachment.

WORKBENCH

Provide freestanding unit of heavy-duty welded steel construction as manufactured by Equipto Storage Products.

Substitutions:

Will be considered by the Project Consultant and Owner when submitted per requirements of Division-0, Division-1, and Section 01630-Product Substitution Procedures.

Size:  34 inch x 72 inch x 37 inch high.

Top:  Steel.

Provide unit with manufacturer’s standard half shelf underneath top.

Prove steel stringer for rigidity.

Finish:  Manufacturer’s standard color finish; color as selected by the Project Consultant.

STORAGE CABINET

Provide cabinet as manufactured by Equipto Storage Products.

Substitutions:

Will be considered by the Project Consultant and Owner when submitted per requirements of Division-0, Division-1, and Section 01630-Product Substitution Procedures.

Twenty two gage steel storage cabinet measuring 48 inch wide x 24 inch deep by 7’-0” high, with built-in lever lock (3-point locking) and 4 adjustable shelves for installation.

Doors rotate on top and bottom pin hinges, swinging a full 180 degrees.

Fully enclosed, 16 gage independent, welded steel frame.

Approximate Weight:  225 pounds.

Finish:  Manufacturer’s standard color finish; color as selected by the Project Consultant.

FLAMMABLE LIQUID STORAGE CABINET

Provide cabinets as manufactured by Justrite.

Substitutions:

Will be considered by the Project Consultant and Owner when submitted per requirements of Division-0, Division-1, and Section 01630-Product Substitution Procedures.

Provide cabinets with the following salient features:

Welded steel construction.

Dual 2-inch vents.

2-inch deep leak proof sill in base of cabinet.

Three-point locking, and concealed, self-closing mechanism.

Fusible Link.

Adjustable galvanized steel shelves with 1/2 inch lip at edges.

Double-wall thermal barrier construction.

Adjustable leveling feet.

EXECUTION

EXAMINATION

Do not proceed with the work of this Section until conditions detrimental to the proper and timely completion of the work have been corrected in an acceptable manor.

INSTALLATION

Set adjustable shelving units accurately in place in locations as indicated on the Drawings.

Touch-up marred surfaces.  Replace units damaged beyond cosmetic correction as directed by the Project Consultant.

Install intermediate shelves at equal spacing in each unit.

Anchor shelving to wall surfaces with anchoring devices as recommended by the manufacturer.

Install cabinets in accordance with manufacturer’s printed instructions.

CLEANING

Clean shelving and cabinets with a damp cloth, leaving them in clean condition, free from dirt, smears, fingerprints and other foreign matter.

END OF SECTION