# SECTION 10820 (22 41 24)

## SHOWER ENCLOSURES

GENERAL

SECTION INCLUDES

Shower Enclosure.

RELATED SECTIONS

Section 04200-Concrete Masonry.

Section 07920-Joint Sealants.

Section 09250-Gypsum Board.

Section 09951-Resinous Flooring.

Section 10810-Toilet Accessories.

Division 15 for plumbing.

REFERENCES

Florida Building Code (FBC), Chapter 11.

SUBMITTALS

Submit manufacturer’s product data describing full range of features, dimension, profiles, installation instructions and maintenance data, also provide the following:

Recycled Content:

Indicate recycled content; indicate percentage of pre-consumer and post-consumer recycled content per unit of product.

Indicate relative dollar value of recycled content product to total dollar value of product included in project.

If recycled content product is part of an assembly, indicate the percentage of recycled content product in the assembly by weight.

If recycled content product is part of an assembly, indicate relative dollar value of recycled content product to total dollar value of assembly.

QUALITY ASSURANCE

Roll-in shower enclosures shall meet accessibility requirements of the FBC Chapter 11.

PRODUCTS

MANUFACTURER

Subject to compliance with requirements, provide products and systems from the following:

Aqua Bath.

Substitutions:

Will be considered by the Project Consultant and Owner when submitted per requirements of Division-0, Division-1, and Section 01630-Product Substitution Procedures.

MATERIALS

All shower enclosure products are to contain recycled content.

Roll-In Shower:  Aqua Bath Model #C6536BF enclosure with the following features:

ADA compliant.

One-piece molded acrylic design.

Class B backside fire rating; flame spread:  less than 30.

Approximate inside dimensions:  60 inch x 36 inch.

Approximate weight:  275 pounds.

Molded soap tray at 24-3/4 inches above the enclosure floor.

Three-sided wrap around grab bar, 1-1/2 inch diameter, 18-gage stainless steel.

Eighteen gage, 1-inch diameter shower curtains rod.

Two wall brackets at 42 inch and 66 inch above the enclosure floor on the back wall for hand held shower.

Self-caulking brass drain.

Completely waterproof.

Full height white vinyl shower curtain and curtain rings.

Roll-In Shower:  Aqua Bath Model #C4136BF-FUS enclosure with the following features:

ADA compliant.

One-piece molded acrylic design.

Class B backside fire rating; flame spread:  less than 30.

Approximate inside dimensions:  36 inch x 36 inch.

Approximate weight:  230 pounds.

Molded soap tray at 28-3/4 inches above the enclosure floor.

Three-sided wrap around grab bar, 1-1/2 inch diameter, 18-gage stainless steel.

Eighteen gage, 1-inch diameter shower curtains rod.

Two wall brackets at 42 inch and 66 inch above the enclosure floor on the back wall for hand held shower.

Self-caulking brass drain.

Completely waterproof.

Full height white vinyl shower curtain and curtain rings.

FINISH

Provide roll-in shower enclosure in one of manufacturer’s standard colors.

Color:  As selected by the Project Consultant.

EXECUTION

INSTALLATION

Install roll-in shower enclosures in accordance with manufacturer’s printed instructions.

Caulk perimeter of enclosure to surrounding wall construction with an acrylic based one-part paint grade sealant.

END OF SECTION