# SECTION 15211 (41 65 13)

## AIR COMPRESSOR

GENERAL

SECTION INCLUDES

Stationary and portable air compressor.

RELATED SECTIONS

Section 15060 - Hangers and Supports

Section 15075 - Mechanical Identification.

Section 15105 - Plumbing Piping.

REFERENCES

ANSI/ASME Section 8D - Boiler and Pressure Vessels Code

ANSI/NFPA 70 - National Electrical Code

QUALITY ASSURANCE

Provide portable air compressor with manufacturer's name, model number and capacity identified.

Ensure products and installation of specified products are in conformance with recommendations and requirements of the following organizations:

ASME

NEMA

UL

SUBMITTALS

Submit product data under provisions of Section 01330 - Submittal Procedures.

Submit manufacturer's installation instructions under provisions of Section 01330-Submittal Procedures.

OPERATION AND MAINTENANCE DATA

Submit operation and maintenance data under provisions of Section 01830-Operation and Maintenance.

Include exploded view and replacement parts lists.

PRODUCTS

ACCEPTABLE MANUFACTURERS

Campbell Hausfeld

Saylor Beall

Ingersoll-Rand

Gardner Denver (Champion)

Quincy

AIR COMPRESSOR                                                                                    (Stationary/Tank Mounted)

Air-cooled, dual-stage, oil lubricated, belt driven reciprocating type air compressor with cast iron cylinders atop a 120 Gallon ASME coded and labeled horizontal receiver.

Provide unit with dry type inlet air filter/silencer, open drip-proof electric motor, dual gauge regulator, pressure gauge, safety valves, drain valve, thermal overload protection, service valve and interconnecting piping between receiver and control.

Piston Displacement:  102 CFM with 175 PSIG operating air pressure.

Normal Operating Pressure:  100 PSIG.

Unit rated for 25 HP, 480 V, 3 Phase, 60 Hz, 1100 RPM.

Model HRA25-152 manufactured by Champion

AIR COMPRESSOR                                                                                                         (Portable/Wheeled)

Air-cooled, single-stage, oil lubricated, belt driven reciprocating type air compressor with cast iron cylinders atop a 20 Gallon ASME coded and labeled horizontal receiver.

Provide unit with dry type inlet air filter/silencer, open drip-proof electric motor, dual gauge regulator, pressure gage, safety valves, drain valve, thermal overload protection, service valve and interconnecting piping between receiver and control.

Piston Displacement:  6.4 CFM with 90 PSIG operating air pressure.

Normal Operating Pressure:  100 PSIG.

Unit rated for 4 HP, 115/230 V, 1 Phase, 60 Hz, 1750 RPM.

Model VT619604AJ manufactured by Campbell Hausfeld.

EXECUTION

INSTALLATION

Coordinate installation with architectural and electrical work.

END OF SECTION