# SECTION 02848 (32 17 13)

## PARKING BUMPERS

GENERAL

SECTION INCLUDES

Precast concrete parking bumpers and anchor pins.

REFERENCES

International Organization for Standardization (ISO) 14021–1999; Environmental Labels and Declarations

SUBMITTALS

Product Data:  Submit product data for all concrete materials, accessories, and admixtures proposed for use including the following information:

Recycled Content:

Indicate recycled content; indicate percentage of pre-consumer and post-consumer recycled content per unit of product.

Indicate relative dollar value of recycled content product to total dollar value of product included in project.

If recycled content product is part of an assembly, indicate the percentage of recycled content product in the assembly by weight.

If recycled content product is part of an assembly, indicate relative dollar value of recycled content product to total dollar value of assembly.

Regional Materials:

Sourcing location(s): Indicate location of extraction, harvesting, and recovery; indicate distance between extraction, harvesting, and recovery and the project site.

Manufacturing location(s): Indicate location of manufacturing facility; indicate distance between manufacturing facility and the project site.

Product Value: Indicate dollar value of product containing local/regional materials; include materials cost only.

PRODUCTS

MATERIALS

All precast products are to contain recycled steel reinforcement, recycled aggregates and materials such as fly ash and granulated ground blast-furnace slag.

Provide 6 foot long reinforced precast parking bumper units with two 5/8-inch diameter precast holes for anchor pins.  Reinforcing shall be one No.4 diameter steel reinforcing bar.

Anchor Pins:  Plain or deformed No. 4 diameter steel reinforcing bars, 12 inches long, conforming to ASTM A 615, Grade 40.

EXECUTION

INSTALLATION

Provide parking bumpers for each stall and anchor pins driven into pavement and made flush with top of bumper.

FIELD QUALITY

Replace broken or damaged bumpers.

END OF SECTION