# SECTION 02890 (34 41 14)

## TRAFFIC SIGNS AND SIGNALIZATION

GENERAL

SUMMARY

The Scope of work of this section includes the provision of various traffic signs throughout Site to ensure safe vehicular and pedestrian traffic.

This Section includes the following:

Aluminum Panel Signs.

Pavement Markings.

Pedestrian Signals assembly, School Flashers, Detector assembly, Mast Arms, Power Supplies and Components.

SUBMITTALS

Product Data:  For each product indicated.

Shop Drawings:  Include plans, elevations, sections, details, wiring diagrams and attachments to other work.

Verify dimensions by field measurements before fabrication and indicate measurements on Shop Drawings.

Provide message list for each sign, including large scale details of wording and lettering.

Samples:  For each sign material indicated that involves color selection.

QUALITY ASSURANCE

Regulatory Requirements:

Signs and Signalization shall conform to Standards of Broward County and Florida Department Of Transportation (FDOT) Standard Index 600-660, 11860-11865, 17302-17346, 17355,17870 and FDOT Specifications and Construction Details.

Coordinate all work to be performed with appropriate approvals from Broward County and local municipal traffic engineering departments.

All Signalization and Warning Flashing Components shall conform to FDOT and Broward County Roadway and Traffic Design Standards and Manual Of Uniform Traffic Devices.

Traffic regulating signs:  Conform to the colors, dimensions and requirements of the Manual on Uniform Traffic Control Devices for Streets and Highways (ANSI D6.1).

Signage and pavement markings:  Conform to FDOT and Broward County Traffic Engineering Department Requirements.

Americans With Disabilities Act (ADA):  Provide conforming pavement markings and signage.

PRODUCTS

MATERIALS:

Sign panels:  Aluminum Association Alloy 6061-T6, .080 gauge, unless otherwise     specified.

Support members:  Aluminum Association Alloy 6061-T6.

Bolts:  Aluminum Association Alloy 2024-T4 with an anodic coating 0.0002 inch thick minimum and chromate sealed.

Lockwashers:  Aluminum Association Alloy 7075-T6 with an anodic coating 0.0002-inch thick minimum and chromate sealed.

Nuts:  Aluminum Association Alloy 6262-T9.

Concrete:  3000 psi at 28 days.

Reflective sheeting:  FDOT Type A.

FABRICATION:

Prepare sign blanks and fabricate reflectorized sign faces to conform to the applicable requirements of FDOT Standard Specifications for Road and Bridge Construction, 1996, Sections 7004 and 700-5.

EXECUTION

INSTALLATION

General:  Locate signs and accessories where indicated, using mounting methods in compliance with manufacturer's written instructions and all applicable codes and Standards of  the FDOT Roadway and Traffic Design Manual.

Install signs level, plumb, and at heights indicated, with sign surfaces free from distortion and other defects in appearance.

FIELD QUALITY CONTROL

Routine inspection of proposed work must be coordinated with Broward County Traffic Engineering and the Broward County School District inspection department.

END OF SECTION